## Slide 1
Mission Analysis in Python
An introduction to Tudatpy
Arnaud MULLER

## Slide 2
Mission Analysis in Python
05/2021
Table of Contents
Introduction
What is Tudat & Tudatpy ?
Tudatpy Workflow
Coding with Tudatpy
Using the documentation
Useful Links
TOLOSAT
1

## Slide 3
Numerical Astrodynamics
Solving differential equations using a numerical integrator
Choosing which equations & models to use
Interpreting, verifying and applying the results
Mission Analysis in Python
Introduction
TOLOSAT
2

## Slide 4
Original project rationale
Validated and modular tool for TU Delft MSc and PhD students doing astrodynamics research
  Validated: all code verified by unit tests
  Modular: flexible setup for diverse applications (re-entry, ascent, transfer design, orbit optimization, …)
  Prevent people from reinventing the wheel
   As an open-source project, has become a more widely-used “software lab” for astrodynamics
Mission Analysis in Python
05/2021
What is Tudat ?
TOLOSAT
3

## Slide 5
Mission Analysis in Python
05/2021
What is Tudatpy ?
TOLOSAT
4
The best way to interact with Tudat
Tudat: core of the software written in C++, performs all the computations
Tudatpy: user-friendly Python interface, keeps the performance of C++
Plotting and analysis of the results can be done directly in Python

## Slide 6
Mission Analysis in Python
Tudatpy Workflow
TOLOSAT
5
Input data (CSV files)
Start/end, step size, spacecraft specs
Integrator settings
Type (RK4, etc.)
Start epoch
Step size
Input Settings
Output Variables
Dependent variables (state in other frames, position of other bodies, etc.)
Dynamics simulator
Type (Single Arc, etc.)
Propagator settings
Type (Translational, etc.)
Initial state
Bodies to propagate
Termination condition
Central Bodies
Earth/Sun/... for each S/C
Body settings
Planetary bodies
Global frame
Bodies
Spacecraft body & specs
Interfaces
Aero, radiation, etc.
Environment
Acceleration models
Bodies to propagate
Central bodies
Acceleration settings
Forces for each S/C

## Slide 7
Mission Analysis in Python
Tudatpy Workflow
TOLOSAT
6
Tudat (C++)
Propagation & other calculations
Tudatpy (Python interface)
Input & Output settings
Tudatpy (Python interface)
Input & Output settings
Results
Seconds since J2000
Cartesian states
Dependent variables
Input settings
Environment
Dynamics simulator

## Slide 8
Select input data
Mission Analysis in Python
Coding with Tudatpy
TOLOSAT
7
Set start & end dates

## Slide 9
Create planetary bodies & set frame
Mission Analysis in Python
Coding with Tudatpy
TOLOSAT
8
Add spacecraft
Define bodies to propagate with respect to which body

## Slide 10
Create aerodynamic & radiation interfaces
Mission Analysis in Python
Coding with Tudatpy
TOLOSAT
9

## Slide 11
Choose acceleration settings
Mission Analysis in Python
Coding with Tudatpy
TOLOSAT
10

## Slide 12
Set initial state of the spacecraft
Mission Analysis in Python
Coding with Tudatpy
TOLOSAT
11
Choose dependent variables to export (on top of cartesian states)

## Slide 13
Create termination condition
Mission Analysis in Python
Coding with Tudatpy
TOLOSAT
12
Create propagator & integrator settings

## Slide 14
Assemble dynamics simulator  STARTS PROPAGATION
Mission Analysis in Python
Coding with Tudatpy
TOLOSAT
13
Extract results

## Slide 15
Tudat documentation
Mission Analysis in Python
Using the documentation
TOLOSAT
14
Useful to understand the intricacies of Tudat and find code snippets.

## Slide 16
Tudatpy API reference
Mission Analysis in Python
Using the documentation
TOLOSAT
15
Useful to see exactly how to use the Tudatpy interface and what features are available.

## Slide 17
References & Links
Dominic Dirkx, AE4868 Numerical Astrodynamics, TU Delft (D.Dirkx@tudelft.nl)
TU Delft Astrodynamics Toolbox (TUDAT) https://docs.tudat.space/en/stable/
Tudat documentation https://docs.tudat.space/en/stable/
Tudatpy API reference https://py.api.tudat.space/en/latest/
Arnaud MULLER